## Slide 1: CHATS Regional ITS Architecture Baseline Inventory Summary
November 2022

## Slide 2: CHATS Regional ITS Architecture Baseline Inventory Summary
For the CHATS Regional ITS Architecture, the following process was utilized to identify projects for the region.
Preliminary Baseline Inventory – Inventory of regional technology deployments that align with the National ITS Architecture Service Packages. Based on existing documentation and feedback from project meetings, interviews, and technical tours.
Gap Assessment – Utilizing the Capability Maturity Model (CMM) the maturity of the region with respect to technology adoption and use was evaluated. The CMM assessment was conducted for six categories Traffic Management Centers (TMC), Traffic Incident Management (TIM), Arterials and Signal Coordination, Traveler Information, ITS and Communications, Emergency Response and Resiliency, and Data Management. Gaps then were identified based on the regional assessment.
Strategy Identification – The gaps fed into the development of specific strategies that are focused on growing the regional maturity in each of the defined categories.
Best Practices – Research efforts identified examples of best practices and projects that were focused on the list of identified strategies. Through conversations with the stakeholders, those strategies were prioritized for the region.
Baseline Inventory Focus Areas – The preliminary baseline inventory then was expanded to integrate more details and refine the existing conditions into Baseline Inventory Focus Areas.
Projects – Based on the prioritized strategies and feedback on the best practices, projects that could build on the existing baseline inventory were identified.
Preliminary Baseline Inventory
Gap Assessment
Strategy Identification
Best Practices
Baseline Inventory Focus Areas
Projects
Process

## Slide 3: Baseline Inventory Focus Areas
Traffic Management Centers
Arterials and Signal Coordination
Real Time at Grade Crossing Information
Performance Measures
Regional Data Flows
ITS Education
Six focus areas were derived based on the prioritized strategies and supported a more focused effort on refining a baseline inventory that could drive the development of technology projects. This plan is the first regional ITS architecture for the region so existing documentation on ITS applications in the region was very segmented and even limited on certain topics.
The preliminary baseline inventory focused on identifying the service packages corresponding to the National ITS Architecture, but this summary focuses on the areas that are most relevant to the region in the next 5 years. The results of the preliminary baseline inventory are summarized in Appendix B. The full results can be seen in the preliminary baseline inventory deliverable. This Baseline Inventory Summary provides a more detailed look at the ITS technology that exists in the defined focus areas listed.
This inventory summary was pulled together based on feedback received during the following meetings:
Core Team Meeting #1
Stakeholder Workshop #1
Core Team Meeting #2
Stakeholder Workshop #2
In addition, supplemental tours and interviews were performed to assist in refining the baseline inventory:
City of Charleston TMC Tour
SCDOT District 6 TMC Tour
SCDOT Statewide TMC Tour
Transdev Dispatch Interview

## Slide 4: Process
Baseline Focus Areas were defined based on the list of prioritized strategies for the region with the intent of refining the details of the baseline inventory in a manner that effectively supports the project development step in the process. Some of the strategies could be grouped and covered by a single baseline inventory focus area (as shown below). Examples of the strategies are given in Appendix A.
TMC’s
Arterials and Signals
Integrated TMC Operations
Sustainable Resources for TMC’s
Integrated Real Time Network Data
Integrated Traffic Management
Dedicated Resources for Operations and Maintenance
Remote Access to Signal Systems
Signal Timing Prioritization Program
Real Time At-Grade Crossing Information
Real Time sharing of at grade crossing information
Performance Measures
Performance Measures Program
Data Flows
Regional Guidance for Assessing and Accessing Data
Existing Education
Education on emerging technologies
Educate leadership to champion the use and funding of technology to assist with active traffic management
Baseline Inventory Focus Areas
Strategy

## Slide 5: Traffic Management Centers
Baseline Inventory - Summary
District 6 TMC
2 operator stations and video wall
Use PAL Guide to enter events and control cameras
Ongoing communication with SHEP drivers as they respond to incidents
Minimal coordination outside of emergency evacuations
Other first responders can operate from the TMC to improve coordination during emergency evacuations
Statewide TMC
4 operator stations (2 utilized, 2 back-up)
Provide coverage for District TMC’s after hours
Have a trainer on staff to train TMC operators and staff
Manage technology including permanent and portable DMS, full color message boards, automated alerts, and cameras.
Ongoing communication with SHEP drivers as they respond to incidents
City of Charleston TMC
2 operator stations and upgraded video wall / TVs (one with Iteris display)
Able to remotely control most signals in the city
Upgrading to MAXVIEW ATMS to collect more data
Limited coordination beyond signal operations, but will increase to support LCRT
Challenges recruiting and retaining operators

## Slide 6: District 6 TMC
Staffing
3 operators through Parsons and 1 SCDOT operator
Staff 12-hour shifts during the week. Typically, 2 operators at a time with staggered shifts
10-hour days on Saturday, 8-hour days on Sunday
Capability to expand to 24-hour operations during an emergency
Handover operations at night to State TMC
Only day off is Christmas
Technology
Use PAL Guide to enter events and control cameras
Access to cameras feeds throughout the state.
Access and control of cameras and DMS in the district to assist with incident response.
Communication via Motorola radios during emergencies
Utilize Iteris Clearguide for network performance data
Video Wall was upgraded in the last 2 years. Limited in controlling which video is shown on the video wall.
Performance Measures
Time on-scene is captured
Have previously tracked some metrics such as time on-scene when reports have been requested
Data capture is less consistent when the report is not requested
Facility
Facility built around 2008
Shared with District Asphalt and Procurement Agency
Small break area for staff
Utilize meeting room overlooking the video wall during evacuations
Sometimes during evacuations Highway Patrol and other first responders will come work out of the meeting room to improve coordination
Tour
Monday, October 17, 2022, 1:00 pm – 1:30 pm
Led by Josh Johnson, SCDOT
Coordination
Utilize TMC meeting room to coordinate with multiple agencies during evacuations and lane reversals
Have ongoing communication with SHEP drivers as they respond to incidents
No collaboration with Charleston TMC
Noted Needs
Camera access and video images experience significant lag time
No automated vehicle location (AVL) technology on SHEP vehicles; Requires constant communication to manage location awareness and dispatch
Extra Iteris display could support visualization of SHEP vehicle locations

## Slide 7: District 6 TMC

## Slide 8: City of Charleston TMC
Staffing
Staff is largely response driven
City has budgeted for a technician role to staff the TMC for 12 hours a day / 5 days a week
A technician is always on-call and the system can be accessed remotely
Technology
City maintains approximately 200 traffic signals
Each controller has its own IP address and the City can pretime them individually or all at once. All equipment runs on 4G.
Most signals are connected with fiber, but a few outlying signals are connected with cellular. The City maintains 19 miles of communications cables and 48 miles of fiber optic cables.
Most of the signals can be remotely controlled from the TMC
City owns 15 cameras and has access to SCDOT cameras
Troy Mitchell and traffic signal technicians receive emails when a signal goes into flash
Battery backups at strategic locations and receive alerts on battery status
Have started installing electronic keys for cabinets. Transition of locks is finished along US-17. Folly Road is planned next.
The City Runs responsive signals along Glenn McConnell Parkway. Folly Road and Maybank Highway are the next two candidates.
Will be upgrading MAXVIEW ATMS later this year. Will be able to add intersection detector sensors and system loops for monitoring and speed data.
Currently, controllers run MAXTIME and are password protected. Can pull up Synchro in MAXTIME software.
Controllers are INTELIGHT. The city does most of the programming.
Controllers run on Linux which is not compatible with SCDOT District 6 systems.
The City will be replacing their Acyclica travel time destination units
The City is working on a connected vehicle pilot
Performance Measures
One of the goals of the TMC is to start tracking performance measures
Would like to use available equipment and software to generate and track performance measures
Facility
Upgraded video wall with new 50” flat-screen monitors a few years ago
TV displaying INRIX Data
Upgraded desks and computers last year
Remodeling based on recommendations from 2017 study - Overview & Assessment of Traffic Signal Operations
Tour
Wednesday, August 24, 2022, 9:00 am – 9:30 am
Led by Troy Mitchell, City of Charleston
Coordination
Do not communicate regularly with the SCDOT District 6 TMC.
Noted Needs
Will need better coordination (cameras, data, etc.) with SCDOT District 6 TMC for the LCRT.
The City is working on a Connected Vehicle pilot project.
The City would like to document and build out its corridors. This year, the City is working on plotting all system routes and speeds
The City has been unable to fill several operator positions. Some of the positions have been open for around two years. They have had difficulty finding candidates to interview.

## Slide 9: City of Charleston TMC

## Slide 10: SCDOT Statewide TMC (Columbia)
Staffing
2 operators staffed during the day
Focus mainly on interstates; Day shift focuses on Columbia area traffic
Greenville, Rock Hill, Myrtle Beach, and Charleston District TMC’s are responsible for their areas from 7:00 am – 7:00 pm 7 days a week
Responsible for the whole state overnight (7:00 pm – 7:00 am; 1 operator and on-calls)
Cover major routes in Myrtle Beach (US 501, SC 31, US 17, and US 17 Bypass) and other areas that play a role during high-profile construction projects
13 total staff (10 operators, 2 managers, 1 trainer/backup operator)
Trainer is responsible for learning new procedures/equipment and disseminating to the rest of the staff
New staff receive 6 weeks of training before being able to work as an operator.
Technology
Communication
SCDOT recently discontinued Highway Advisory Radio alerts for emergencies. They will be focusing on social media and subscription-based text messages.
Formal agreements allows operators to listen to all emergency radios around the state
Forward SLED alerts such as Amber Alerts, Endangered person alerts, and Blue alerts
Can post messages on 90 permanent and more than 100 portable DMS
About 70 of the portable DMS get used during hurricane evacuations
5 full-color message boards
SCDOT has automated alerts for emergencies, construction, weather, and incident and congestion notices (travel time alerts) using their automated ATMS software.
Utilize 511SC to communicate with the public. Also utilize social media, but do not monitor messages from the public on social media.
Push automated weather-related messages
SHEP
Constant communication between SHEP and the Statewide TMC
Covers specific metro areas 7 days / week between 7:00 am and 7:00 pm
Can support some significant construction projects 24/7
Primary goal is to clear the roadway including moving cars out of the roadway
Work Zones
Responsibility of the contractor on major projects
“Smart ITS” includes end of queue warnings, travel time impacts, and lane closure notifications
Data Sources
Over 600 cameras statewide. Camera access via SCDOT’s CLARIS platform
Cameras have a slow load time and can only be controlled by SCDOT staff.
Handful of portable work zone cameras that utilize cell signal (can be unreliable)
None of the cameras are equipped with night vision
Video sharing agreements for emergency responders to have access cameras
Separate APIs for sharing video images with the media/ public
Have wind/fog sensors but would like some backup data sources
Use Iteris Clear Guide and Google Maps to monitor real-time traffic flows
SCDOT ATMS maintains a database of incidents
Tour
Monday, September 26, 2022, 10:00 am – 11:00 am
Led by Jennifer Rhoades, SCDOT

## Slide 11: SCDOT Statewide TMC (Columbia)
Coordination
Do not coordinate with municipal TMC’s.
Noted Needs
The Statewide TMC is maturing to the point where they need to coordinate with municipal TMC’s. Want to help municipalities manage downstream consequences of incident related detours prompted by SCDOT.
Hiring for the TMC has been difficult. Factors include pay, demand for complex multi-tasking, computer and radio skills, non-standard hours, and handling difficult scenarios.
SCDOT wants to be able to communicate to drivers how to avoid an incident prior to reaching it and at what location the incident clears.
Need access to municipal traffic cameras
Back-up wind and fog sensors
Need access or implementation of more flood sensors
Performance Measures
Some performance measures including incident clearance times, number of calls to SHEP, type of assistance provided, number of SHEP stops made, and number of events entered by TMC operator.
Facility
Statewide TMC is considered part of SCDOT headquarters
4 operator stations; 2 stations are backups
IT Division supports Statewide TMC but they do not operate 24/7
Servers are split between two circuits for redundancy
Statewide TMC conference room acts as an Emergency Operation Center. Accommodates SCDOT, Highway Patrol, National Guard, and other responders
Full kitchen to support staffing hours during an emergency and late-night shifts
Planning for a new facility in the next 5 years

## Slide 12: Traffic Management Centers – Gap Assessment
Definition: Traffic Management Centers have two key operational functions: real-time active monitoring and coordination, and traffic management strategy implementation. These functions are accomplished by both staff and systems. TMCs provide a safer transportation system for users by being both responsive to incidents and innovative in technologies to accomplish that goal. | 
What is placing us in our current tier? | What is keeping us from advancing to the next tier?
Current Traffic Management Centers include the Statewide Traffic Management Center (Columbia), SCDOT District 6 TMC (Charleston), and City of Charleston Traffic Management Center (Charleston). SCDOT manages interstate travel solely. CCTV cameras provide surveillance capabilities. Some processes are documented but the documents are outdated. Statewide ITS Architecture is from 2015 and systems engineering process is applied sometimes. Local TMC has staffing shortages. Interagency collaboration is minimal. | Limited funding for TMC Operations, with no SCDOT funding beyond interstate operations Limited documentation or standardized processes for local TMC operations Systems engineering process not fully mainstream Agency decisions not driven by performance measures Challenges around staff retention and training. Unclear roles and few full-time staff dedicated to ITS at the local level. SCDOT has ITS staff and funding, but funding and staffing does not provide for growth. Agencies primarily focus on the TMC role for specific events. Limited capacity in staffing and experience to fully recognize benefits of TMC coordination across multiple agencies.
 | Level 1 (Ad-hoc) | Level 2 (Managed) | Level 3 (Proactive) | Level 4 (Fully Collaborative)
Business Processes | Ad-hoc planning for TMC functions, vision not well defined; TMC processes specific to SCDOT are not documented | Some planning for asset management; processes for specific corridors or region, but not consistent statewide; some TMC processes documented | TMC operations needs captured in budget, standardized processes, consistent review/update of TMC strategic direction | TMC vision is integrated in all aspects of DOT business; Planning for Operations is standard practice; asset lifecycle cost is part of five-year programming processes; processes are regional
Systems and Technology | Ad hoc approaches to system implementation; systems engineering (SE) not applied consistently; procurement processes; ITS architecture is outdated; individual systems that are not integrated | Some elements of SE are used, including ConOps, architectures, developed and documented with costs included; TMC monitors some field systems; SE process applied to some aspects of TMC operations; some emerging technology considerations | Systems, technology standardized and integrated on a regional/corridor basis; statewide SOPs updated used; integrated statewide network; SE process is mainstreamed into TMC business practices; integrated systems | Architectures and technology routinely upgraded to improve performance; systems integration/ interoperability maintained on continuing basis; Strong support for adopting advanced technologies
Performance Measurement | Some outputs measured and reported for some aspects of TMC operations; typically, historical performance information | Some elements of TMC performance are tracked and reported; focus is primarily on usage/activity reports assessing trends; some real-time data is used for operational decision-making at the TMC | Performance outcomes guide recommend operational improvements; real-time data routinely used for decision-making; TMC uses some real-time data from other centers/sources | Operational decisions based on multi-jurisdictional real-time information; performance management strategy guides innovation at the TMC.
Culture | Individual staff champions promote operations; TMC operations priorities based primarily on champion focus areas; TMC not often included in work zone (WZ) or event planning, incident debriefing, etc. | Role of TMC acknowledged but connection to core ops areas is not always recognized; TMC engaged in pre-planning for WZ, TIM and PSE based on individual relationships | TMC is a core program, region values TMC role and input to key processes, TMC operating needs factored in early as part of other planning/scoping decisions | TMC highly integrated with many processes, region sees TMC as a valuable asset, high value on TMC data
Organization and Staffing | Individual staff champions promote operations; TMC functions learned mostly OJT; career path for TMC is limited and not well defined | Core KSA’s identified and help support TMC ConOps; roles for in-house and contractor staff are defined; some training, but limited external training opportunities; communication between DOT and contractors is fragmented and event-based | TMC career path is clearly defined; established and successful training program; performance standards are clear and documented; good communication between staff and contractors | Commitment to ongoing training and professional development; strong retention of staff due to career path and advancement opportunities; strong and well-known performance standards
Collaboration | Relationships ad hoc, and on personal basis (public-public, public-private) | Collaboration with external partners is formal, and usually driven by specific needs, TMC roles still fragmented and event-based; real-time collaboration with public safety for incidents | Multi-agency and coordinated operations for planned events; some partnerships for key corridors; TMC role defined and understood | Multi-agency response strategies are mainstreamed into TMC operations; operating processes and procedures documented and used frequently

## Slide 13: Traffic Management Centers – Strategy Identification
Challenges around staff retention and training
Limited funding for TMC Operations
Agencies primarily focus on the TMC role for specific events
Agency decisions not driven by performance measures
Gaps
Technical Training Curriculum
Sustainable Resources for TMCs
Regional Performance Measures Program
Strategies
Integrated TMC Operations
Project List
Next Step
Discrete TMC Focused Projects
Risk Identification

## Slide 14: Arterial and Signal Coordination
Baseline Inventory - Summary
City of Charleston
Manages approximately 200 traffic signals
Most signals are connected with fiber, and some are connected with cellular
Upgrading to an ATMS system
Manages on-call for signal retiming
Staffing constraints for reviewing timing plans
SCDOT District 6
Manges approximately 275 traffic signals
Some signals are connected with fiber, and some are connected with radio
Manages cameras and DMS on interstate
Manages on-call for signal retiming
Staffing constraints for reviewing timing plans
City of North Charleston
Manages approximately 40 traffic signals
Signals are not connected to communications
City does not perform regular retiming
City does not have engineers on staff to perform signal designs
Town of
Mt. Pleasant
Manges approximately 60 traffic signals
City maintains some communications between signals
The City maintains coordination and some cameras
The City is working on a project to implement EVP

## Slide 15: City of Charleston
Signals
City maintains approximately 200 traffic signals
Each controller has its own IP address, and the City can pretime them individually or all at once. All equipment runs on 4G.
Receive emails when a signal goes into flash
Battery backups at strategic locations and receive alerts on battery status
Have started installing electronic keys for cabinets. Transition of locks is finished along US-17. Folly Road is planned next.
The City Runs responsive signals along Glenn McConnell Parkway. Folly Road and Maybank Highway are the next two candidates.
Will be upgrading MAXVIEW ATMS later this year. Will be able to add intersection detector sensors and system loops for monitoring and speed data.
Currently, controllers run MAXTIME and are password protected. Can pull up Synchro in MAXTIME software.
Controllers are INTELIGHT. The city does most of the programming.
Controllers run on Linux which is not compatible with SCDOT District 6 systems.
Manages an on-call for signal retiming. Have staffing constraints to review timing plans.
Due to the grid on the peninsula, they must update the plans more wholistically or in large portions at a time. Did a large update in 2018.
With the large amount of growth, they should be retiming more frequently.
Fiber / Communications
Most signals are connected with fiber, but a few outlying signals rely on cellular communications.
The City maintains 19 miles of communications cables and 48 miles of fiber optic cables.
Other Technology
City of Charleston TMC
City owns 15 cameras and has access to SCDOT cameras
The City will be replacing their Acyclica travel time destination units
SCDOT District 6
Signals
Manages approximately 275 signals
District 6 maintains about 20 coordinated corridors
Aims to retime signals every 3 years however does not always happen
Use consultants to prepare retiming plans
Internally, there are limited staff cannot maintain pace to manage consultants and review plans timely.
Inconsistencies between plans produced by consultants.
There are no standards for signal timing
District 6 maintains some agreements with municipalities for signals maintenance
Fiber / Communications
Have some fiber and radios to connect some signals
Have remote access to approximately half of the signals
Other Technology
District 6 TMC
TMC monitors and controls SCDOT cameras during operating hours
TMC manages DMS on the interstate

## Slide 16: City of North Charleston
Signals
City maintains approximately 40 signals
SCDOT signals in North Charleston are maintained by the city through an agreement.
The North Charleston maintenance agreement is the only agreement that does not include engineering.
The city does not perform regular arterial retiming. Only look at timings in response to citizen complaints.
City does not have remote access to signals.
City does not have engineers on staff to perform signal designs.
Some adaptive signals along Patriot Boulevard.
Fiber / Communications
Signals are not connected to communications.
Other Technology
Town of Mount Pleasant
Signals
Town maintains approximately 60 signals
Town maintains coordination.
Have not used real time data for signal timing
Utilizes InSync coordination system (adaptive signals) along several corridors.
Project to implement EVP for emergency vehicles. Full implementation by 2023.
Fiber / Communications
Town maintains some communications between signals
Other Technology
The Town has some cameras and is working to get access to other cameras utilized by police department

## Slide 17: Arterial and Signal Coordination
Definition: Arterial & Signals Management focuses on signalized arterial routes which play a significant role in the performance of SCDOT’s comprehensive transportation network. Some of these arterial networks are managed through centralized signal systems that span signalized intersections on multiple corridors, but an even greater number are managed by interconnected coordinated signal systems located on a single corridor. Arterial management emphasizes signal operations, timing strategies, and performance measures. |  |  |  | 
 | What is placing us in our current tier? |  | What is keeping us from advancing to the next level? | 
 | Multiple agencies have a program for signal maintenance. Before and after travel time runs assess signal timing project implementations (considers emissions, delay, and travel times). Extension of staff expands the resources available to perform traffic signal coordination. Standard practices exist for design and operations within each agency. Some adaptive signal systems in place. |  | Limited collaboration between freeway and arterial management. Funding and staffing constraints limit the effectiveness of achieving optimal signal coordination, management, and performance. SCDOT and maintaining agencies are currently unable to remotely manage traffic signal systems. Local funding primarily focused to expanding roadway capacity. No routine updates for signal plans Limited signal timing projects are coordinated for routes that cross multiple jurisdictions. | 
 | Level 1 (Ad-hoc) | Level 2 (Managed) | Level 3 (Proactive) | Level 4 (Fully Collaborative)
Business Processes | Traffic signal management program business decisions and resource allocations are ad hoc and/or compliant driven. Allocation of resources is focused primarily on keeping the traffic signal system functioning, but not necessarily at its optimum level of performance. | Traffic signal management planning, design, operations, and maintenance decision-making generally operate in silos and are not well integrated. Resource allocation decisions are focus primarily on maintaining reliability of infrastructure. | Traffic signal management decision-making is objective-based. The region has business processes that are flexible to adjust and trade-off resource allocations to extend good basic service beyond traditional operating conditions. | Traffic signal management decision-making is performance-based and multimodal. The region has the ability to replace equipment and systems technologies based on end-of-life predictions.
Systems and Technology | Traffic signal systems and technologies limit the region's ability to provide good basic service. Systems and technologies have limited capabilities to remotely manage, operate, and maintain the system. Limited use of system engineering concepts has resulted in the procurement of an array of systems and technologies with incompatible features and functions. Management and maintenance of systems and technologies is primarily complaint-driven. | The region has the capability to identify malfunctions and manage operations limited to specific intersections or corridors. The region can achieve consistency in design and operations through standard practice. The region routinely deploys advanced signal timing concepts (such a volume density, traffic responsive, actuated coordination, etc.) to achieve operational objectives and can implement pre-planned responses to planned and unplanned events. Tracking of assets and work items performed primarily through spreadsheets. | Traffic signal infrastructure is connected to a management system which can alert operators to equipment malfunctions as assist with managing timing plans. The region has capability to remotely manage that system, but management decisions are operator-driven with little automated decision support. Consistency in design and operations is achieved through the use of standard designs and hardware specifications. Systems and technology can support pre-planned responses and advanced concepts such at transit signal priority, work zone management, etc. | The region has the capability to dynamically respond to changing operational conditions to support the needs of all stakeholders to meet operational objectives. The region is able to automatically identify and respond to service disruptions and can reestablish continuity of service remotely. Procurement policies and practices support the procurement products and technologies that represent "best value" for achieving design and functional consistency. Consistency of design and operations is achieved the application of system engineering processes.
Performance Measurement | Performance measures are not connected to regional goals and objectives. Instead, use of performance measures is limited to special studies (upon request by administration or confirm reported operational deficiency). Performance measures are not used to proactively locate where operations and maintenance issues exist. Productivity is evaluated by tracking activities (e.g. number of maintenance call received, number of signals retimed, etc.) | The region has defined performance measures to assess project implementations (such as before/after evaluations). The region may collect output-oriented performance measures for operations and maintenance activities. Operational and management decisions are based on periodic manual observations in the field. | The region has defined performance measures to assess project implementations. The region uses outcome-oriented performance measures for operations and maintenance activities. Operational and management decisions are based on real-time, high-quality data accessible from remote locations. | Region has defined performance measures to assess system performance. System performance is monitored on regular, on-going basis. Automated systems are often used to collect and assess system performance. Performance data is used to identify performance and efficiency trends. The region uses performance to better allocate resources, identify maintenance deficiencies, and equipment failures, etc.

## Slide 18: Arterial and Signal Coordination
Culture | Traffic signal management does not have a champion or core group within the region that can promote traffic signal operations and maintenance concerns and priorities. Leaders have shared responsibilities with other core agency functions. Outreach to stakeholders and media occurs on an ad hoc basis. Region does not any have standardized approaches for communicating with public and policy makers | Traffic signal management is recognized as one of many functions within the region, but no special emphasis placed on performance. The region supports teams dedicated traffic management functions, but no broad acknowledgement or awareness by leadership as to what they do. Outreach to the public and policy maker regarding traffic signal operations occurs on an as needed basis, primarily related to projects. | Traffic signal management acknowledged as important function by regional decisions makers. Traffic signal management champion resides at decision-making level. Regular outreach occurs to communicate with policy-makers regarding traffic signal operations through traditional means (reports, fact sheets, etc.). | Region viewed as a progression region by peers and the entire program staff can serve as a champion for the traffic signal operations issues and concerns. Regional staff is unified as to the goals, objectives, and priorities of the region and uses them to drive decision-making. Programs can still function at high level, even with the departure of key leaders. The region seeks opportunities to proactively promote region's mission, goals, and objectives in person before advisory groups, citizenry, and policymakers through both traditional and non-traditional (social media, dashboards, etc.) communications media.
Organization and Staffing | Staff maintains minimum level capabilities necessary to do the job. This limits the agencies to assign staffing resources only to limited number of activities. Often, engineering and technical staff have other responsibilities other than traffic signal operations. | Key staff is well versed on basic signal timing design and operational concepts. Work force development efforts are focused on raising the level of competency of the staff. Programs within agencies reside in structured silos (planning, design, maintenance, operations, etc.) with limited coordination between silos. | Staff is well versed in both basic and advanced traffic signal control and management concepts and can execute solutions on existing technologies. Workforce development efforts focus on expanding breadth of competencies and providing redundancy in core competencies. The agencies can dedicate staff resources to high priority corridors/areas on a limited basis. | Staff is highly motivated and qualified and has the capability to develop and deploy innovative solutions to complex operational situations. Workforce development efforts focus on providing a nimble workforce that has the ability to adapt to different situations, depending on the needs of the region. The region uses a matrix approach to managing traffic signal operations. Staff has capability to perform activities across network and across functional units.
Collaboration | No data sharing exists between regional partners. Collaboration with internal and external stakeholders is rare, often forced upon agencies by policymakers or administrators. | Information and data are archived internally and shared upon request with other stakeholders. The agency collaborates with internal and external stakeholders on a case-by-case or project basis, but these collaborations are not sustained over time. | Formal and well-documented archiving system is used to store collected data. Data can be quickly and easily accessed through well-documented and standardized electronic format, easy to use by all partners. The regional agencies seek collaborations with other transportation stakeholders that to capitalize on opportunities to satisfy needs of operational objectives. | The regional agencies routinely collaborate with internal and external stakeholders (e.g., fire, police, transit, advocacy groups, etc.) that allow them to capitalize on opportunities to satisfy needs of multiple stakeholder objectives. Data is shared in real-time with regional operating partners and is used to support numerous regional activities (such as regional planning models, support real-time traveler information displays, etc.).
 | Level 1 (Ad-hoc) | Level 2 (Managed) | Level 3 (Proactive) | Level 4 (Fully Collaborative)

## Slide 19: Arterial and Signal Coordination – Strategy Identification
Project List
Next Step
Discrete Arterial and Signal Coordination Focused Projects
Risk Identification
Limited collaboration between freeway and arterial management
Funding and staffing constraints
SCDOT and maintaining agencies are currently unable to remotely manage traffic signal systems
No routine updates for signal plans
Gaps
Integrated Traffic Management
Remote Access to Signal Systems
Strategies
Dedicated Resources for ITS Operations and Maintenance
Regional Signal Timing Standards
Limited signal timing projects are coordinated for routes that cross multiple jurisdictions

## Slide 20: Charleston County TRAINFO Pilot
Real Time at Grade Crossing Information
Baseline Inventory - Summary
Current Status
Charleston County has partnered with TRAINFO to study the use of their sensors to identify when at-grade railroad crossing are closed.
Closures cause significant delays to vehicles, transit, and emergency responders.
The goal of the pilot is to provide better at-grade crossing status data so transit operators and emergency dispatch can reroute vehicles and mitigate delays.
County has currently deployed 3 sensors. Preparing to deploy 4 additional sensors in North Charleston and Charleston through FRA partnership.
The data has been integrated into the Alastar system for Charleston County.
BCDCOG FRA CRISI Grant Application
Need
Multiple stakeholders, including the City of Charleston, CARTA, and first responders, have expressed an interest in expanding this pilot and gaining access to the data.
Transit notes that gate activations at at-grade crossings impact bus schedules and can delay buses for more than 30 minutes from the documented schedule.
Other first responders would like to have similar data to improve response time.
Real time activation information could be provided to drivers through DMS or other alert systems to allow passenger cars to also reroute.
Agencies discussed other data sources such as signal preemption data or transit logs that could be leveraged to study the impacts or potential schedules for at-grade crossings.
Current Status
BCDCOG is pursuing a Grant to expand the TRAINFO pilot throughout the region.
The application is due in December 2022.
The goal of the project is to collect data on at-grade crossings to reduce transportation delay experienced by transit, first responders, and drivers.
Need
Data can be leveraged by fleet managers for transit vehicle optimization, dispatch centers for first responders, and transportation agencies to notify the public.
CARTA Swiftly Data
Current Status
CARTA uses the Swiftly System which collects data on buses utilizing trackers.
Data supports the analysis of bus delays experienced due to the activation of at-grade crossings
CARTA has years of data collected by the systems

## Slide 21: Real Time at Grade Crossing Information
Project List
Next Step
Discrete Real Time at Grade Crossing Information Focused Projects
Risk Identification
Standalone traveler information systems that are not connected or integrated
Gaps
Strategies
Real time sharing of at grade crossing information

## Slide 22: Performance Measures
Baseline Inventory - Summary
City of Charleston TMC
Does not track performance measures
Has a desire to start tracking performance measures
CARTA
Monitoring some performance measures including:
  Bus Capacity (Full Buses)
  Delays
    Start time of delay
    End time of delay
    Reason for delay (train, congestion, incidents, etc.)
    Bridge
  Bus detours
  Driver “call-offs”
  Bus swaps (mechanical issues, biohazard accidents)
  Wheelchair user denials of lap belt
Desired Data
  Flooding information
  Police arrival times
  Train blockages
Statewide TMC
Monitors some performance measures including:
  Incident clearance times
  Number of calls to SHEP
  Type of assistance provided
  Number of SHEP stops made
  Number of events entered by TMC operator
BCDCOG / CHATS
Champion Performance Measure use to support data driven decisions
SCDOT District 6 TMC
SHEP time on scene is entered into their systems
Past years they tracked some metrics for reports when asked

## Slide 23: Performance Measures – Strategy Identification
Agency decisions not driven by performance measures
Gaps
Limited Performance Measures
Limited Performance Measures
Limited use of performance measures to support AARs and future technology implementations
Limited capacity in staffing or skills to coordinate or support data integration
Limited capacity in staffing or skills to coordinate or support data integration
Category
Traffic Management Centers
Traffic Incident Management
Traveler Information
Emergency Response and Resiliency
Data Management
Project List
Next Step
Discrete Performance Measure Focused Projects
Risk Identification

## Slide 24
Weather Sensors
Alastar program
  Combined data sources including flooding/king tide sensors, camera feeds, emergency vehicle location data, and operates as an “operating theater”
District 6
  Road temperature sensors with sharing capabilities
  Benefits seen with the potential of sharing wind data and ice sensors for maintenance and road condition awareness
City of Charleston
  TIDEeye outlines flooded areas
  Compatible with Waze and can notify alerts through app
SCDOT uses technology resources such as portable changeable message signs, cameras, congestion motoring and SHEP during inclement weather emergencies
Flood sensors could be an additional benefit to CARTA as flooding becomes more of a concern
  Can help communicate potential stops that might be skipped
Baseline Inventory - Summary

## Slide 25: Transit
Baseline Inventory - Summary
CARTA
Services the tri-country area with 25 routes
  Regular Routes
  Express Routes
  Downtown Area Shuttles (DASH) Routes
  Airport Route
  CARTA OnDemand (partnership with Uber to serve seniors and Tel-A-Ride paratransit customers)
Veolia dispatching software used
  Drivers sign into Syncromatic software through an on-board tablet that integrates with the vehicle head box and fare box
  CARTA Swiftly software shows vehicle locations
Existing automated voice enunciator and visual display for next stop incorporated on some buses
Performance Monitoring Criteria
  Full Buses
  Delays (Start time of delay, end time of delay, reason for delay – train/congestion/incidents/bridge/if detoured)
  Driver “call-offs” (drivers unable to work because of sickness/absence)
  Bus swaps for mechanical issues or biohazard accidents
  Wheelchair user denials of lap belt
Lowcountry Rapid Transit (LCRT) - In Planning Development
Proposed to be a 21.3-mile rapid transit system
68 existing signalized intersections proposed in Charleston, North Charleston, and Ladson
30% design plans and cost estimates submitted to Federal Transit Administration (FTA) January 2022
FTA has approved the project to enter the New Starts Engineering phase of the Capital Investment Grants Program in July 2022
In November 2022, an intergovernmental agreement (IGA) was signed between BCDCOG, SCDOT, Charleston Country, and CARTA
Transit Signal Priority is a tactical focus that supports the goal of the LCRT
  Process by which transit vehicles are given operating priority through a signalized intersection
  Priority is achieved through an extension of green time when an approaching bus is behind schedule

## Slide 26: Freight and Port Management
Millions of freight tons (worth $B) travel the region’s multimodal freight transportation infrastructure annually
  Approximately 38% of the region’s economy
  Approximately 18% of the state’s economy
Multimodal network provides BCD businesses with access to domestic and global supplies, facilities, and markets
79% of freight tonnage moves through the region via trucks
  The remaining 21% is transported via rail
Possible truck technology applications
  CV technology to support truck platooning on portions of I-26
  Freight Signal Priority
  Truck Parking facilities
    MAASTO truck parking study (requirement being to implement the technology to the field)
Potential for federal funding through FAST Act (ATCMT grant program)
Baseline Inventory - Summary
Freight Status
Port Status
23 million tons of freight moves through the Port of Charleston
Automated solutions within the existing terminal facilities can provided significant benefit
  Containers can be more efficiently stacked to increase facility capacity
  Containers can be more quickly located to reduce container dwell time
Cameras on inbound lanes provide traffic conditions on port’s website
License Plate Reading (LPR) technology at port gates to efficiently validate vehicles
Project funding for Smart Striping pilot project approved
  Data built in to road striping and structures along the roadway provide constant communication and navigation within the port facility
  Located on port property (Wando facility – 3 locations)
  Pilot will assess durability and cost effectiveness through partnerships with SC Ports Authority, SC Research SCRA, Charleston County, and the Ray
Need for technology-based wayfinding within the port property
  Technology would address safety concerns and mobility challenges experienced by commercial vehicle drivers trying to navigate within the property
  Proposed solution is Waze for Ports

## Slide 27: Data Flows
Baseline Inventory - Summary
City of Charleston TMC
City Camera Feeds
Signal in flash notification
Alastar
SCDOT Camera Feeds
Battery backup status
MAXVIEW ATMS (proposed)
INRIX Data
City of Charleston TMC
Background
The City of Charleston TMC utilizes a variety of data sources
The Data Flows identified throughout the project are shown in the diagram below

## Slide 28: SCDOT Statewide TMC
Baseline Inventory - Summary
SCDOT Statewide TMC
SLED Alerts
ATMS System
Weather Data
SCDOT Camera Feeds
Portable Work Zone Camera Feeds
Wind / Fog Sensors
Iteris ClearGuide Data
Incident Data
On-scene reports from SHEP
Background
The SCDOT Statewide TMC utilizes a variety of data sources
The Data Flows identified throughout the project are shown in the diagram below

## Slide 29: SCDOT District 6 TMC
Baseline Inventory - Summary
SCDOT District 6 TMC
SCDOT Camera Feeds
Iteris ClearGuide Data
On-scene reports from SHEP
Incident Data
Background
The SCDOT District 6 TMC utilizes a variety of data sources
The Data Flows identified throughout the project are shown in the diagram below

## Slide 30: CARTA
Baseline Inventory - Summary
CARTA
Swiftly bus tracking data
SCDOT video feeds
Passenger counts
Start/End time of delay
Delay reason
Bus Detour
Driver Attendance
Bus Swap Reasons
Wheelchair user denials of lap belt
Background
CARTA utilizes a variety of data sources
The Data Flows identified throughout the project are shown in the diagram below

## Slide 31: Alastar
Baseline Inventory - Summary
Alastar
SCDOT Camera Feeds
Real time bus locations and routes
DHEC Camera Feeds
Charleston County Schools Camera Feeds
NOAA Weather Data
River Gauges
Wind Gauges
TRAINFO Sensors
Emergency Vehicle Locations
Road Closures
Critical Infrastructure
Background
Alastar is a system utilized by the consolidated dispatch units for Charleston County, Berkely County and Dorchester County.
The platform was first utilized by Charleston County Consolidated Dispatch to bring together disparate data sources from a variety of agencies into one platform.
BCDCOG is facilitating the integration of the Alastar systems between the 3 counties.
The platform is used for high-level viewing of incidents
The platform can be shared with other agencies such as first responders.
A special media page has also been set up to improve communication with the media during incidents.
The Data Flows integrated into Alastar are shown in the diagram below.

## Slide 32: Data Flows
DATA MANAGEMENT |  |  |  | 
Definition: Data Management includes all activities related to collecting, storing, and using data. It also addresses procedures around data security, integration, and resiliency. Data collection should be efficient and effective; analysis should support an overall performance management program, and efforts should clearly align with achieving the region’s identified objectives. |  |  |  | 
 | What is placing us in our current tier? |  | What is keeping us from advancing to the next level? | 
 | SCDOT maintains the TEAMS database for signals inventory. Partner agencies can request and gain access. Some SCDOT GIS datasets are available to be shared with external partners. The Alastar system integrates data from multiple sources within individual counties. Data security protocols are coordinated at the individual agency level. HERE data feeds travel time calculations. Some agencies are partnering to integrate data from Waze through Public Partnerships Program. Existing statewide data procured and shared (RITIS, ClearGuide) |  | Limited guidance or standards for how to acquire, access, or share data externally. Both institutional and physical obstacles impede regional partners from gaining access to datasets owned by other agencies. There are limited processes for data validation and maintenance. Not all agencies use data to inform decisions and develop performance measures. Limited training for staff on accessing and validating data. Limited capacity in staffing or skills to coordinate or support data integration. Differing security requirements between agencies. | 
 | Level 1 (Ad-hoc) | Level 2 (Managed) | Level 3 (Proactive) | Level 4 (Fully Collaborative)
Business Processes | There are no formal guidelines on how data is acquired, stored, or shared. Contracts with private sector data providers are ad hoc. | There is limited formal guidance on how data is acquired, stored, or shared internally. Contracts with private sector data providers reflect regional agency needs. | There is formal guidance on how and where data is acquired, stored, or shared both internally and externally. Contracts with private sector data providers align with regional objectives. | Guidance on how and where data is acquired, stored, and shared both internally and externally is institutionalized. Contracts with private sector data providers are well integrated and common practices.
Systems and Technology | There is a lack of awareness of the existing data for both internal and external use. Maintenance is non-existent or occurs when issues are encountered. | The data is not easily accessible and may be housed in multiple locations at the agency level. Maintenance may occur occasionally. Individual datasets exist but are not integrated. | The data is housed in multiple locations at the agency level but easily accessible by partner agencies. Maintenance of the data systems occurs often. Some datasets are integrated. | The data is well-integrated and housed in a single location that is easily accessible by multiagency staff. Data repository undergoes routine maintenance. Redundancy of central data supports continuity.
Performance Measurement | Data is not readily available to inform data-driven decisions. The data is not validated through a formal process. | The data is occasionally used to inform data-driven decisions. There is a lag in accessibility for the most recent data. Data validation occurs on an individual level. | The data supports data-driven decisions that align with regional goals. There is a data validation process in place. | The data is comprehensive and supports data-driven decisions that align with multiagency objectives. There is a well-integrated data validation process.
Culture | Leadership does not recognize the value of acquiring, purchasing, or investing in new or existing data sources. The data acquisition process is not well-funded to keep up with regional needs. | Leadership seldom recognizes the need to acquire, update, and validate data sources. With limited resources, agencies must “make-do” with available information. | Leadership understands the need for more funding to acquire relevant and recent data. The region has some funds to invest in new data tools or sources. | Leadership advocates for more funding to further the available data for multiagency use. The region actively invests in using and purchasing the latest data sets.
Organization and Staffing | There is informal training on where and how internal and external data is housed. | There is some training that provides all internal staff with knowledge of where to find data. There may be some guidance on validating sources internally and externally, but that process is not formalized. | Training is updated to reflect the latest data management processes which all staff are encouraged to take. Regional leadership encourages the use of cross-cutting data sources. | Regional leadership actively invests time and resources to promote new efficiencies. All staff are encouraged to participate in training that is updated frequently to reflect enhanced processes.
Collaboration | Agencies maintain individual datasets focused on their individual objectives. | Some internal and external coordination occurs for data alignment and limited data integration. Data security protocols and data management are coordinated at the individual agency level. | Significant internal and external coordination occurs for data integration. Some consistency in data security protocols. | There is multiagency consistency in data security protocols and data management. Cross-cutting performance driven decisions are made in the larger interest of the agency or region.
The Data Flows Baseline Inventory Focus Area is derived from the Data Management Strategies. The CMM matricie for Data Management is included below.

## Slide 33: Data Flows – Strategy Identification
Project List
Next Step
Discrete Data Flow Focused Projects
Risk Identification
Limited guidance or standards for how to acquire, access, or share data externally
Gaps
Regional Guidance for Acquiring, Accessing, and Sharing Data
Strategies

## Slide 34: ITS Education
Baseline Inventory - Summary
Statewide TMC
Has a trainer on staff for the TMC
Trainer is responsible for learning new procedures / equipment and disseminating to the rest of the staff
New staff receive 6 weeks of training before being able to work as an operator.
ITS Education – Strategy Identification
Category
Gap
Strategy
Technical Training Curriculum
Traffic Management Centers
Challenges around staff retention and training
Education on Emerging Technologies
ITS and Communications
Local staff mostly focused on signals, fiber optic cables, and cameras but not broader ITS applications
Education on Emerging Technologies
Emergency Response and Resiliency
Limited use of technologies beyond foundational ITS infrastructure during emergencies
Educate leadership to champion the use and funding of technology
Emergency Response and Resiliency
Limited understanding from leadership on technology investments to support emergency response

## Slide 35: ITS Education – Best Practices Summary
Example: AZTech Workforce and TSMO Development
Developed a database that includes resources for certifications and training.​
Certifications and training resources are identified for each position.​
Database includes course length, costs, links, and process to obtain certifications.
Technical Training Curriculum
Example: Partnering with Professional Organizations
SC Section ITE – https://www.scsite.org/
ITS Carolinas – https://itscarolinas.org/
ITS America – https://itsa.org/
National Operations Center of Excellence – https://transportationops.org/
  Talking TIM Webinars – https://transportationops.org/tim/talkingtim
Transportation Communications Newsletter
  http://transport-communications.blogspot.com/
FHWA
  Facilitating Integrated ITS Deployment Program – https://ops.fhwa.dot.gov/int_its_deployment/standards_imp/training.htm
Consortium for Innovative Education (CITE) – https://www.citeconsortium.org/
Education on Emerging Technologies
Example: Holly Springs Emerging Transportation Technologies Vision
Chapter in Holly Springs Comprehensive Transportation Plan
Emerging Technologies Toolbox
Helps decision makers know what they should start considering and preparing for
Provides connection between CTP and future ITS Master Plan
Example: ITS Heartland’s TSMO University
Roadmap for TSMO awareness
Train the Trainer program
Website includes TSMO information: standards, guidelines, materials, and webinars
Educate Leadership to Champion the Use and Funding of Technology
Example: TSMO Awards, National Operations Center of Excellence
Awarded annually to individuals and organizations championing TSMO
Help celebrate wins
Give leadership examples of success to help support funding

## Slide 36: Project List
Next Step
Discrete ITS Education Focused Projects
Risk Identification

## Slide 37
Staffing and Procurement
Unable to optimize the use of existing equipment due to staffing shortages
Open positions remain unfilled for over a year
HR dictates title and salaries and are unable to match market salary/contributions
Balancing staffing and managing funds has been a challenge with limited senior mentorship
Imbalance in workload overwhelms staff and can create a decline in morale
Qualified Products List (QPL)
  New products are sent to SCDOT QPL and Preventative Maintenance Operations Program
  QPL submissions are reviewed by consultants on the Signal On-Call with typical 90 day turn around
Innovative Projects List (IPL)
  Managed by SCDOT QPL and Preventative Maintenance Operations Program
  Created over 5+ years ago
  One or two products on the list at a time
  Specifications are developed while the product is on IPL
Vendor/Municipality Involvement
  SCDOT cannot purchase new equipment to test and evaluate
    Process requires municipalities to purchase and test new products
    Vendors can submit paperwork and get products approved for the IPL for highlighted and specific project needs
      Recent Success – GridSmart (Greenville)
      In development – MioVision (Myrtle Beach)
    After testing and review of the project, support to the product can be done by placing onto the QPL
  Vendors can donate equipment for short term testing
    Agreements are in place to allow this partnership
    Procurement language includes language to protect SCDOT QPL office from misuse by vendors (damaged equipment, unanticipated bills, etc.)
Baseline Inventory - Summary
Equipment Procurement Processes
Staffing Summary

## Slide 38: References
The following sources were gathered to complete the Preliminary Baseline Inventory and Baseline Inventory Summary for the region.
Source Name | Year | Owner | Data Type
BCDCOG Walk Bike Master Plan | 2016 | BCDCOG | Document/Report
CHATS Congestion Management Process | 2018 | BCDCOG | Document/Report
BCDCOG Regional Transit Framework Plan | 2018 | BCDCOG | Web Page
BCDCOG Regional Park-and-Ride Study | 2018 | BCDCOG | Web Page
CHATS 2040 Long-range Transportation Plan | 2019 | BCDCOG | Document/Report
CHATS Public Participation Plan | 2019 | BCDCOG | Reference
BCDCOG Rural Workforce Transportation Study | 2020 | BCDCOG | Document/Report
TSP Concept of Operations Report - DRAFT | 2021 | BCDCOG | Document/Report
Automated Traffic Signal Performance Measures (ATSPM) Development | 2021 | BCDCOG | Reference
Concept of Operations (DRAFT) - BCDCOG Dorchester Road Transit System Signal Prioritization Project | 2021 | BCDCOG | Document/Report
Dorchester Road Transit Signal Priority (TSP) Signal Inventory Report (2021) | 2021 | BCDCOG | Reference
Dorchester Road Transit Signal Priority (TSP) Network Assessment | 2021 | BCDCOG | Reference
Traffic Signal Optimization Report - BCDCOG Dorchester Road Transit System Signal Prioritization Project | 2021 | BCDCOG | Document/Report
BCDCOG Transit and Bus Stop Design Guidelines | 2021 | BCDCOG | Document/Report
BCDCOG Regional Freight Mobility Plan - Final Report | 2021 | BCDCOG | Document/Report
BCDCOG Rural Long Range Transportation Plan | 2022 | BCDCOG | Web Page
CARTA Battery Electric Bus Master Plan - Final Report | 2022 | BCDCOG | Document/Report
BCDCOG Human Services Coordinated Transportation Plan | 2022 | BCDCOG | Document/Report
Low county Rapid Transit Website |  | BCDCOG | Existing Project
US 52 Corridor Study | Ongoing | BCDCOG | Web Page
BCDCOG Ongoing Transportation Projects Interactive Map | Ongoing | BCDCOG | Web Page
TriCounty Link Website |  | BCDCOG | Reference
BCDCOG TriCounty Link App |  | BCDCOG | Application
BCDCOG CARTA Validation of Automated Passenger Counters |  | BCDCOG | Data Source
BCDCOG Bicycle and Pedestrian Count Data |  | BCDCOG | Data Source

## Slide 39: References
Source Name | Year | Owner | Data Type
BCDCOG/CHATS Congestion Management Process | Ongoing | BCDCOG/CHATS | Document/Report
BCDCOG Beach Traffic Cameras |  | BCDCOG/Municipalities | Web Page
CARTA Battery Electric Bus Master Plan - Final Draft Report | 2022 | CARTA | Document/Report
CARTA Mobile Ticketing |  | CARTA | Application
CARTA Transit App |  | CARTA | Application
CARTA Fares and Passes |  | CARTA | Web Page
CARTA Safety and Security |  | CARTA | Web Page
RCN Technologies |  | CARTA | Web Page
Charleston County Comprehensive Plan | 2018 | Charleston County | Document/Report
Charleston Consolidated 911 Center |  | Charleston County | Web Page
CHATS Regional ITS Architecture - Core Team Meeting #1 Meeting Minutes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - Core Team Meeting #2 Meeting Minutes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - Stakeholder Workshop #1 Meeting Minutes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - Stakeholder Workshop #2 Meeting Minutes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - City of Charleston TMC Tour Notes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - District 6 TMC Tour Notes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - SCDOT Statewide TMC Tour Notes | 2022 | CHATS | Document/Report
CHATS Regional ITS Architecture - Transdev Dispatching Interview Notes | 2022 | CHATS | Document/Report
City of Charleston Traffic Sequencing Plan (2008) | 2008 | City of Charleston | Document/Report
City of Charleston Existing Fiber Network | 2011 | City of Charleston | Document/Report
City of Charleston Rethink Folly Road: A Complete Streets Study | 2016 | City of Charleston | Document/Report
City of Charleston Proposed Fiber Network | 2016 | City of Charleston | Document/Report
An Overview and Assessment of Traffic Signal Operations | 2017 | City of Charleston | Document/Report
Traffic Signal Retiming Report & Traffic Signal Operations Assessment | 2017 | City of Charleston | Document/Report
City of Charleston Citywide Transportation Plan | 2018 | City of Charleston | Document/Report
City of Charleston Septima Clark Pkwy - Signal Retiming Report | 2018 | City of Charleston | Document/Report
Potential ITS Projects Letter | 2019 | City of Charleston | Reference
City of Charleston Comprehensive Parking Study | 2019 | City of Charleston | Document/Report

## Slide 40: References
Source Name | Year | Owner | Data Type
City of Charleston Proposed Fiber Network | 2020 | City of Charleston | Document/Report
City of Charleston Traffic Controllers Asset List | 2020 | City of Charleston | Document/Report
City of Charleston City Plan | 2021 | City of Charleston | Document/Report
City of Charleston Climate Action Plan | 2021 | City of Charleston | Document/Report
City of Charleston SmartCard Parking Program |  | City of Charleston | Web Page
City of Charleston Traffic Management Center website |  | City of Charleston | Web Page
City of Charleston Peak Volume Maps |  | City of Charleston | Map
City of Charleston Traffic Cabinets Asset List |  | City of Charleston | Document/Report
City of Charleston Traffic Management Center Description |  | City of Charleston | Document/Report
Charleston Emergency Management |  | City of Charleston | Web Page
Truck Route Analysis for City of North Charleston | 2015 | City of North Charleston | Document/Report
Naval Base Intermodal Container Transfer Facility Surface Transportation Impact Study | 2019 | City of North Charleston | Document/Report
National Infrastructure Protection Plan (2006) | 2006 | Department of Homeland Security | Document/Report
SCDOT HOV/HOT Lane Feasibility Study | 2010 | SCDOT | Web Page
North CHATS Area Traffic Signal Master Plan Draft | 2011 | SCDOT | Document/Report
North CHATS Area Traffic Signal Master Plan Final | 2013 | SCDOT | Document/Report
North CHATS Area Traffic Signal Master Plan | 2013 | SCDOT | Document/Report
SCDOT TMC Standard Operating Guidelines (SOG) | 2014 | SCDOT | Document/Report
SC Statewide ITS Architecture | 2015 | SCDOT | Document/Report
SCDOT’s Adaptive Signal System Safety Impacts report | 2021 | SCDOT | Document/Report
511 Tools |  | SCDOT | Data Source
SCDOT I-26 Corridor Management Plan | Ongoing | SCDOT | Web Page
SCDOT I-526 Lowcountry Corridor | Ongoing | SCDOT | Web Page
South Carolina Statewide Truck Parking Assessment Study (Draft Final) | Ongoing | SCDOT | Document/Report
SCDOT’s I-526 Intersection Improvement Project |  | SCDOT | Existing Project
SCDOT STIP |  | SCDOT | Web Page
SCDOT TEAMS - Signal Inventory |  | SCDOT | Data Source
SCDOT Emergency Response |  | SCDOT | Web Page
SHEP Patrol Routes |  | SCDOT | Web Page
SCEMD Hurricane Traffic Management |  | SCDOT/SCDPS/SCEMD | Web Page
South Carolina Hurricane Plan | 2022 | SCEMD | Reference
SC IPAWS |  | SCEMD | Web Page

## Slide 41: References
Source Name | Year | Owner | Data Type
Town of Mt. Pleasant - Traffic Preemption Devices | Ongoing | Town of Mt. Pleasant | Web Page
Effective Traffic Control Letter for the Cities of North Charleston, Summerville; surrounding cities; and Charleston & Dorchester Counties | 2017 | Town of Summerville | Reference
Summerville Police Communications |  | Town of Summerville | Web Page
Summerville Police General Services |  | Town of Summerville | Web Page
2015 Urban Mobility Scorecard | 2015 | Texas A&M Transportation Institute and INRIX | Reference
National ITS Architecture | 2021 | USDOT | Reference

## Slide 42: APPENDIX
Appendix A – Strategy Examples
Sustainable Resources for TMC’s
Integrated Real Time Network Data
Integrated Traffic Management
Dedicated Resources for Operations and Maintenance
Remote Access to Signal Systems
Signal Timing Prioritization Program
Real Time sharing of at grade crossing information
Performance Measures Program
Regional Guidance for Assessing and Accessing Data
Education on emerging technologies
Educate leadership to champion the use and funding of technology to assist with active traffic management
Integrated TMC Operations
Examples include increased sharing and integration between TMC’s by co-locating agencies.
Examples include plans for establishing reliable resources such as funding and staffing.
Examples include using real-time data sources to inform operators and traffic management staff of the transportation network’s real-time performance.
Examples include Integrated Corridor Management with signal timing flush plans, traveler information, and CCTV monitoring across jurisdictions.
Examples include statewide and regional maintenance contracts, grant funding, and internal roles focused on ITS.
Examples include local agencies sharing access to their signals with the State TMC after hours.
Examples include prioritization tools to assess corridors across jurisdictional boundaries and a plan for proactively updating signal timing plans.
Examples include using real time at-grade crossing status to determine impacts on transit or emergency responder routes and alert or reroute drivers.
Examples include dashboards for real-time arterial performance measures, updating crash reports to capture data for performance measures, and including performance measures in after action reviews.
Examples include data flow documentation and connection security plans.
Examples include being involved in the evolution of the industry through professional organizations (webinars, lunch and learns, conferences, etc. ), peer exchanges, and ITS integration with other planning documents.
Examples include training for leadership, celebrating wins, and communicating performance.

## Slide 43: Appendix B – Preliminary Baseline Inventory Summary Table
Legend |  | 
 | Status | Status Description
 | E - Existing | In operation, constructed
 | C - Committed | Funded but not built, committed to be constructed or placed into operation
 | P - Planned | Identified in a plan or designed, does not need to be funded, expected to occur in next 5 years
 | - | Not Planned - Does not exist or is not planned in the next 5 years
 | N/A | Not something they managed by this agency